#### ROTOMATIC – standard version

Standard version is in text marked extra bold.

# Basic parameters

| environment | according to HD60364-5-51:2009 | normal, AA5+AB5 |
| --- | --- | --- |
|  | according to EN 60721-3-3 | 3K3/3B1/3C1/3S1/3M1 |
|  | workplace | covered, protected against weather |
|  | temperature | +5ºC to +40ºC |
|  | rate of temperature change | max. 0.5ºC/min. |
|  | relative humidity | 5% to 85% |
|  | altitude | up to 2000 m |
|  | explosive environment | no (prohibited) |
|  | area around machine | EN 547-1, EN 547-2, EN 547-3 |
|  | interference elimination | group 1 class B according to EN 55011 |
|  | interference resistance | EN 61000-4-2, EN 61000-4-3 EN 61000-4-4, EN 61000-4-6 |
| operating staff | age | 18 and more |
|  | burden | 17 kg (reel with film during loading) |
|  | acquaint with user manual | obligatory |
| revision | initial revision from manufacturer | IEC 364-6-61 |
|  | revision before operating | IEC 364-4-41, IEC 364-6-61 |
| CE certification |  | yes for all versions |
| service life |  | 50 000 hours |

|  | 1700 | 2300 | 3000 |
| --- | --- | --- | --- |
|  | Basic | Standard | Profi | Standard | Profi | Standard |  |
| pneumatic | supply pressure | 0.6 ÷ 1.5 MPa |
|  | working pressure | 0.5 MPa |
|  | air consumption | ca 2 l /cycle (supporting air blowing for top sheet app. ca 100 l /cycle) | ca 2 l /cycle (supporting air blowing for top sheet app. ca 200 l /cycle) |
| dimension of pallet | min. | 600 × 600 mm | 900 × 900 mm | 900 × 1200 |
|  | max. | 1250 × 1250 mm | 1600 × 1600 mm (1200 × 1900 mm) | 2100 × 2100 mm (1200 × 2400 mm) |
|  | min. height of goods | 500 mm (1000 mm with to sheet) |
|  | max. height of goods | see table Height of goods |
| wrapping foil | diameter of reel | max. 250 mm |
|  | width of foil | 500 mm |
|  | diameter of tube | 75 ÷ 77 mm |
|  | length of tube | 500 ÷ 515 mm |
|  | height of reel | ca 17 kg |
|  | thickness | 20 – 40 µm |
|  | material of foil | PE (stretch film) |
|  | min. stretchness | 150% (Manuli AT, ATX, MET1) |
| top sheet film | diameter of reel | max. 300 | max. 300 |
|  | width of reel | max. 1600 | max. 2200 |
|  | weight | max. 80 kg | max. 100 kg |
|  | thickness | 50 – 80 µm |
|  | material of film | PE |
| el. installation | power supply | TNC-S 3+PE+N 3×400/230V, 50Hz ČSN EN 50160 (EN 50160) |
|  | power requirement | 16 kVA *) | 17 kVA *) |  | 17 kVA *) |  |
|  | protection | 50 A *) | 50 A *) |  | 63 A *) |  |
|  | p. supply of control circuit | 24V= |
| shielding | motors | IP55 |
|  | switch boxes | IP54 |
|  | sensors | IP65 |
|  | collectors | IP20 |
|  | ending equipment (welding) | IP00 |

*) Parameters above are valid for basic version of machine: Rotomatic with one motor prestretch unit without conveyors.

Feasible combination of  Rotomatic equipment

|  | 1700 | 2300 | 3000 |
| --- | --- | --- | --- |
|  | Basic | Standard | Profi | Standard | Profi | Standard |  |
| Prestretch device | 1M | Yes | Yes | Yes | Yes | Yes | Yes |  |
|  | 1M-R | No | Yes | Yes | Yes | Yes | Yes |  |
|  | 1MD | No | Yes | Yes | Yes | Yes | Yes |  |
|  | 1MD-R | No | Yes | Yes | Yes | Yes | Yes |  |
|  | 2MD | No | Yes | Yes | Yes | Yes | Yes |  |
| Ending mechanism - welding | Yes | Yes | Yes | Yes | Yes | Yes |  |
| Top sheet | No | Yes | Yes | Yes *) | Yes *) | Yes *) |  |
| Top-platen | No | Yes | Yes | Yes *) | Yes *) | Yes *) |  |
| Air holder | No | Yes | Yes | Yes *) | Yes *) | Yes *) |  |
| Pallet lift | Yes | Yes | Yes | Yes *) | Yes *) | Yes *) |  |
| Conveyors | Yes | Yes | Yes | Yes | Yes | Yes |  |

*) The possibility of equipment must be accepted by manufacturer.

Prestretch devices:

1M	One-motor prestretch device, controlled by switch lever

1M-R	One-motor prestretch device, controlled by switch lever, optionally with the contracting of foil into rope. Foil is extended at the beginning and ending of packing (radio data communication)

1MD	One-motor prestretch device, digitally controlled - by encoder (radio data communication)

1MD-R	One-motor prestretch device, digitally controlled - by encoder, ptionally with the contracting of foil into rope. Foil is extended at the beginning and ending of packing (radio data communication)

2MD	Two-motor prestretch device, digitally controlled - by encoder (radio data communication)

# Suppliers of component parts

| pneumatics |  | FESTO |
| --- | --- | --- |
| control system | PLC | Simatic S7 – 300 |
|  | operator panel | Siemens: OP 7, , MT057 TST (touch screen) |
| radio data communication |  | LG System |
| sensors |  | Telemecanique |
| power supply |  | WAGO |
| contactors |  | Telemecanique |
| circuit breakers |  | Merlin Gerin |
| motor protection switch |  | Merlin Gerin |
| main switch |  | Sontheimer |
| auxiliary relays |  | Schrack, Telemecanique |
| safety relays |  | Pizzato, Leuze |
| distribution frame |  | WAGO |
| controllers |  | Telemecanique |
| frequency converters |  | Telemecanique |
| motors | ring lifting | SEW |
|  | ring | Siemens |
|  | prestretch | Siemens, Lenze |
|  | ending of foil | Bonfiglioli |
|  | top sheet application unit | Bonfiglioli |
|  | top-platen | Bonfiglioli |
| cable chains |  | Flexa |

# Security

## Security category

| according to EN 13849-1 | PL=d |
| --- | --- |
| demand on category used in project | 4 |

## Recommended security

| prevention of entrance | safety fences |
| --- | --- |
| Emergency stop push buttons | security module Pizzato |
| fences doors | electromechanic lock |
| feed-in conveyor | safety light barriers Leuze |
| feed-out conveyor | safety light barriers Leuze |

## Time needed to stop machine after pressing emergency stop button

|  | 1700 | 2300 | 3000 |
| --- | --- | --- | --- |
| Basic | 2 s | --- |  |
| Standard | 2 s | 3 s |  |
| Profi | 3 s | 4 s |  |

# Colour design

| frame | RAL 9006 silver |
| --- | --- |
| moving parts | RAL 1018 yellow |
| switchbox cabinet | RAL 7035 grey |
| others | RAL 9005 black - galvanized and plastic parts without colouring |

# Transport dimensions

| Type | 1700 | 2300 | 3000 |
| --- | --- | --- | --- |
| length without top sheet applicator | mm | 2875 | 3740 | – *) |
| length with top sheet applicator | mm | 3165 | 4055 | – *) |
| width | mm | 2400 | 3130 | – *) |
| height with top-platen | mm | 2380 (2790) | 2380 (2790) | – *) |
| switch box cabinet | mm | 2150 (2000 cabinet + 150 base) |
| drop | mm | 400 | 400 | 400 |
| width | mm | 1000, 1200 | 1000, 1200 | 1000, 1200 |

*) Rotomatic 3000 is transported unassembled

# Heights of goods and wrapping

## Height of the machine for certain heights of goods and design

Determination of height of the machine:

VZ	-	Height of goods together with pallet

VD	-	Height of conveyor

HHZ	-	dimension from table of basic heights (according to dimensions, equipment and way of wrapping)

VSZ	-	basic height of machine (value from the same row as HHZ)

## Table of basic heights of machines

## ROTOMATIC 1700 BASIC, STANDARD, prestretch unit with 1motor and 1Mdriven – basic dimensions

| additional equipment | Max. height to upper edge of goods together with conveyor [mm] - HHZ | Height of machine [mm] - VSZ | skeleton |
| --- | --- | --- | --- |
| top sheet app. | Mechanical top-platen | scissors top-platen | supporting air blowing | lifting eq. for pallets | ending of film upwards | Ending of film downwards | pallet depart by 90° |  |  |
|  |  |  |  |  | 1900 | 2100 | 1750 | 3370 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1750 | 1950 | 1750 | 3370 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1540 | 1740 | 1390 | 3370 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1390 | 1590 | 1390 | 3370 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1800 | 2000 | 1650 | 3800 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1650 | 1850 | 1650 | 3800 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1840 | 2040 | 1690 | 3370 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1690 | 1890 | 1690 | 3370 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1700 | 1900 | 1550 | 3800 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1550 | 1750 | 1550 | 3800 | Skeleton 1700/1,55m |

## ROTOMATIC 1700 PROFI, prestretch unit 1M, 1M driven, 2M – basic dimensions

| additional equipment | Max. height to upper edge of goods together with conveyor [mm] - HHZ | Height of machine [mm] - VSZ top sheet app. | skeleton Mechanical top-platen |
| --- | --- | --- | --- |
| top sheet app. | Mechanical top-platen | scissors top-platen | supporting air blowing | top sheet app. | Mechanical top-platen | scissors top-platen | supporting air blowing |  |  |
|  |  |  |  |  | 1790 | 1990 | 1640 | 3400 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1640 | 1840 | 1640 | 3400 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1430 | 1630 | 1280 | 3400 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1280 | 1480 | 1280 | 3400 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1690 | 1890 | 1540 | 3800 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1540 | 1740 | 1540 | 3800 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1730 | 1930 | 1580 | 3400 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1580 | 1780 | 1580 | 3400 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1590 | 1790 | 1440 | 3800 | Skeleton 1700/1,55m |
|  |  |  |  |  | 1440 | 1640 | 1440 | 3800 | Skeleton 1700/1,55m |

## ROTOMATIC 2300 STANDARD, PROFI, prestretch unit 1M and 1M driven – basic dimensions

| additional equipment | Max. height to upper edge of goods together with conveyor [mm] - HHZ | Height of machine [mm] - VSZ top sheet app. | skeleton Mechanical top-platen |
| --- | --- | --- | --- |
| top sheet app. | Mechanical top-platen | scissors top-platen | supporting air blowing | top sheet app. | Mechanical top-platen | scissors top-platen | supporting air blowing |  |  |
|  |  |  |  |  | 1900 | 2100 | 1750 | 3680 | skeleton 1700/1,55m |
|  |  |  |  |  | 1750 | 1950 | 1750 | 3680 | skeleton 1700/1,55m |
|  |  |  |  |  | 1540 | 1740 | 1390 | 3680 | skeleton 1700/1,55m |
|  |  |  |  |  | 1390 | 1590 | 1390 | 3680 | skeleton 1700/1,55m |
|  |  |  |  |  | 1800 | 2000 | 1650 | 4080 | skeleton 1700/1,55m |
|  |  |  |  |  | 1650 | 1850 | 1650 | 4080 | skeleton 1700/1,55m |
|  |  |  |  |  | 1840 | 2040 | 1690 | 3680 | skeleton 1700/1,55m |
|  |  |  |  |  | 1690 | 1890 | 1690 | 3680 | skeleton 1700/1,55m |
|  |  |  |  |  | 1700 | 1900 | 1550 | 4080 | skeleton 1700/1,55m |
|  |  |  |  |  | 1550 | 1750 | 1550 | 4080 | skeleton 1700/1,55m |

Bold – standard solution

PPV	-	necessary height (supplemental)

PPV = VZ + VD – HHZ

In table supplemental heights of skeletons can be found nearest higher supplemental height of skeleton PV (PPV < PV)

## Supplemental heights of skeletons

| skeleton | supplemental height of skeleton - PV |
| --- | --- |
| Skeleton xxxx/1,55m | 0 |
| Skeleton xxxx/1,8m | 250 |
| Skeleton xxxx/2,05m | 500 |
| Skeleton xxxx/2,3m | 750 |
| Skeleton xxxx/2,55m | 1000 |
| Skeleton xxxx/2,8m | 1250 |

VS	-	height of machine

VS = VSZ + PV

*) Min. ceiling height of hall on the assembly place = height of machine VS+200

## minimal height of goods (min. height of wrapped goods together with pallet)

| equipment | minimal height of goods [mm] |
| --- | --- |
| without top sheet app. | 500 (without conveyor) |
| with top sheet app. | 1000 (without conveyor) |

## Bottom border of film

(minimal bottom border of film above  bottom border of pallet)

| version | bottom border of film [mm] |
| --- | --- |
| ROTOMATIC | 1700 | 2300 | 3000 |
| standard without pallet lifting device | 105 ÷ 125 (according to stretchness of film and dimensions of goods) | cca. 150 (according to stretchness of film and dimensions of goods) | cca. 150 (according to stretchness of film and dimensions of goods) |

If there is demand for wrapping of goods together with pallet is necessary to use pallet lifting device

## Height of conveyor

|  | height of conveyor [mm] |
| --- | --- |
| standard | 500 |
| min. | 100 |

## Standard wrap and wrapping capacity

Definition:

- Single wrap:wrapping only one way when prestretch device move up or down

- Cross wrap: two ways wrapping when prestretch devidce move up and dowm (both direction)

- Dustproof: top-sheet foil is below wrapping foil (into the goods)

- Waterproof: top-sheet foil is between two layers of wrapping foil

| Wrap type | single wrapping |
| --- | --- |
| Start the wrapping | at the top | at the bottom |
| top-sheet | without top-sheet | dustproof | without top-sheet |  | waterproof |
| number of coils – at the top | 2 | 2 | 2 |  | 4 |
| number of coils – at the bottom | 2 | 2 | 2 |  | 2 |

| Wrap type | cross wrapping |
| --- | --- |
| Start the wrapping | at the top | at the bottom |
| top-sheet | without top-sheet | dustproof | waterproof | without top-sheet | waterproof |
| number of coils – at the top | 3 | 3 | 4 | 2 | 4 |
| number of coils – at the bottom | 2 | 2 | 2 | 3 | 3 |

Vertical shift of foil (pitch) / 1 rotation of the ring

for rotation speed = 100%, lifting speed = 100%)

|  | pitch [mm] / 1 rotation of the ring |
| --- | --- |
| ROTOMATIC | 1700 | 2300 | 3000 |
| BASIC | 318 | - | - |
| STANDARD | 275 | 275 | 275 |
| PROFI | 275 | 275 | - |

Standard value of pitch quarantees minimal overlapping 80 mm.

Calculation of coil number:

VZ	-	height of goods incl. pallet [mm] (when pallet lift is in use, add 150mm)

ON	-	number of coil at the top

OD	-	number of coil at the bottom

S	-	pitch  [mm]

Number of coil (single wrapping) = VZ/S+ON+OD

Number of coil (cross wrapping) = 2*VZ/S+ON+OD

(VZ/S round up at whole number)

## Standard assembly drawing Rotomatic 1700

# Weights

| skeleton | extenders | 1.55 | 1.8 | 2.05 | 2.3 | 2.55 | 2.8 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 1700 Standard | 1005 kg | 1030 kg | 1060 kg | 1085 kg | 1125 kg | 1145 kg |  |
|  | 1700 Profi | 1055 kg | 1080 kg | 1110 kg | 1140 kg |  | 1195 kg |  |
|  | 2300 Standard |  |  |  | 1565 kg |  |  |  |
|  | 2300 Profi |  |  |  | 1575 kg |  |  |  |
|  | 3000 Standard |  |  |  |  |  |  |  |

| frame |  | 1700 | 2300 | 3000 |
| --- | --- | --- | --- | --- |
|  | Standard | 200 kg | 285 kg | 500 kg |
|  | Profi | 200 kg | 285 kg |  |

| Prestretch device (together with ring and counterweight) |  | 1700 | 2300 | 3000 |
| --- | --- | --- | --- | --- |
|  | Standard 1M | 270 kg | 275 kg | 280 kg |
|  | Standard 1M-R | 275 kg |  |  |
|  | Profi 1M | 308 kg | 280 kg |  |
|  | Profi 2M | 375 kg |  |  |

| ending of foil |  | 1700 | 2300 | 3000 |
| --- | --- | --- | --- | --- |
|  | standard | 70 kg | 80 kg | 85 kg |
|  | side |  | 60 kg |  |

| top sheet applicator |  | 1700 | 2300 | 3000 |
| --- | --- | --- | --- | --- |
|  |  | 120 kg | 175 kg | 205 kg |

| top-platen |  | 1700 | 2300 | 3000 |
| --- | --- | --- | --- | --- |
|  | mechanical | 120 kg |  |  |
|  | scissors | 205 kg | 210 kg | 245 kg |

| supporting blower for top sheet |  | 1700 | 2300 | 3000 |
| --- | --- | --- | --- | --- |
|  |  | 20 kg | 75 kg | 30 kg |

| electro cabinet | 2000x800x400 | ca 300 kg according to equipment of machine |
| --- | --- | --- |
|  | 2000x1000x400 | ca 350 kg according to equipment of machine |
|  | 2000x1200x400 | ca 400 kg according to equipment of machine |

| driven conveyor Rotomatic |  | 900 | 1100 | 1200 | 1300 |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | standard 3000 | 265 kg | 295 kg | 310 kg |  |  |
|  | standard 4000 |  |  |  |  |  |
|  | standard 4500 |  |  |  |  |  |

| driven conveyor | width | 900 | 1100 | 1200 | 1300 | 1400 |
| --- | --- | --- | --- | --- | --- | --- |
|  | length 1330 | 125 kg |  |  |  |  |
|  | length 1500 | 135 kg | 165 kg | 175 kg |  |  |
|  | length 2000 | 190 kg | 210 kg |  |  |  |
|  | length 2500 | 225 kg | 255 kg |  |  |  |
|  | length 3000 | 265 kg |  |  |  |  |

| pallet lifting device | 900 | 195 kg |
| --- | --- | --- |
|  | 900/250 | 440 kg |
|  | 1200 with tilting support of big pallets | 350 kg |
|  | 1200 without tilting support of big pallets | 340 kg |

| safety fences | fence part 995 (+ column) | 22 kg |
| --- | --- | --- |
|  | 815 (+column) | 20 kg |
|  | 545 (+ column) | 15 kg |
|  | door right ,left | 50 kg |
|  | double wing door | – |

| service foot bridge | 1700 |  |
| --- | --- | --- |
|  | 2300 | 175 kg |
|  | 3000 | 200 kg |

# Parameters of parts of machine

## Ring

| type | 1700 | 2300 | 3000 |
| --- | --- | --- | --- |
|  | Basic | Standard | Profi | Standard | Profi | Standard |  |
| outer diameter of ring | mm | 2400 | 3000 | 3700 |
| inner diameter of area for pallet at rotation | mm | 1760 | 2300 | 3000 |
| revolutions | 1/min | 22.6 | 40 | 60 | 32 | 50 | 30 |  |
| motor power | kW | 2x0.75 | 2x1.5 | 2x0.75 | 2x1.5 | 2x1.5 |  |

## Lift

| type | 1700 | 2300 | 3000 |
| --- | --- | --- | --- |
|  | Basic | Standard | Profi | Standard | Profi | Standard |  |
| speed of stroke | m/s | 0.12 | 0.18 | 0.27 | 0.14 | 0.23 | 0.14 |  |
| motor power | kW | 1.5 | 3 | 2.2 | 4 | 3 |  |

## Prestretch device

| type |  | Basic 1M | Standard 1M | Profi 1M |  | Standard 2M | Profi 2M |
| --- | --- | --- | --- | --- | --- | --- | --- |
| regulation of pre-stretch of film |  | 1 motor + transmission |  | 2 motors |
| motor power | kW | 0.75 3x400/230V | 1.1 127/230 V |  | 1.25 / 1.8 | 1.8 / 2.5 |
| primary pre-stretch | % | 80, 120, 160, 210, 290 | 80÷300 |
| change of pre-stretch ratio |  | change of belt and pulley | regulation of motor |
| secondary pre-stretch | % | 60 ÷ 200 *) |

*) Limiting values depends on used material (foil) and way of wrapping

## Top-platen mechanical

| type | 1700 | 2300 | 3000 |
| --- | --- | --- | --- |
|  | Basic | Standard | Profi | Standard | Profi | Standard |  |
| dimensions of pressing board | mm | – | 1000x600 | – | – |
| pressing power | kg | - | 70 | – | – |

## Top-platen scissors type

| type | 1700 | 2300 | 3000 |
| --- | --- | --- | --- |
|  | Basic | Standard | Profi | Standard | Profi | Standard |  |
| motor power | W | - | 750 |
| dimensions of pressing board | mm | - | 1000x600 | 1000x600 | according to contract |
| max. pressing power without supporting air blowing | kg | - | 100 | 100 | - |
| max. pressing power with supporting air blowing | kg | - | 120 | 120 | - |

Pressing power is regulable.

# Additional equipment

## Driven conveyor

| type | Roto | standard |
| --- | --- | --- |
| width | mm | 900 | 1100 | 1200 | 900 | 1100 | 1200 | 1300 | 1400 |
| nominal length |  | 3000 (for ROTO 1700) 4000 (for ROTO 2300) 4500 (for ROTO 3000) | 1350 1500 2000 2500 3000 | 1500 2000 | 1500 |  |  |
| height | mm | optionally (350, 480, 530, 580, 630) ± 60 |
| diameter of rollers | mm | 80 |
| spacing | mm | 182.5 | 166.5 |
| motor |  | 550W / 3x400V 50Hz |
| chain |  | 10B |
| maximum load | kg | 1600 | 1500 | 1500 | 1600 | 1500 | 1500 |  |  |
| speed | m/min | 12 |

## Pallet lifting device

| to roller conveyors | 900 | 900 |  |  |
| --- | --- | --- | --- | --- |
| air | MPa | 0.6 ÷ 1 | 0.6 ÷ 1 |  |  |
| supplier of pneumatics |  | FESTO | FESTO |  |  |
| height min. | mm | 450 ÷ 575 (during assembly) | 450 ÷ 575 (during assembly) |  |  |
| height max. | mm | 600 ÷ 725 | 600 ÷ 725 |  |  |
| stroke of pallet | mm | 140 | 140 |  |  |
| air consumption |  | ca 6 l per stroke | ca 6 l per stroke |  |  |
| speed of stroke |  | 3-6 according to load and air supply | 3-6 according to load and air supply |  |  |
| max. load | kg | 1200 | 1200 |  |  |
| max. width of lifting d. | mm | 860 | 860 |  |  |
| width of lifting plinth | mm | 860 | 860 |  |  |
| nr. of solid plinths |  | 3 | 5 |  |  |
| nr. of tilting plinths |  | – | – |  |  |
| spacing of solid plinths | mm | 380 (outer 760) | 190 (outer 760) |  |  |
| spacing of tilting plinths | mm | – | – |  |  |
| length of proper lifting d. | mm | 1084 | 1084 |  |  |
| width of pallet min. –max. | mm | 600 ÷ 900 | 600 ÷ 900 |  |  |
| length of pallet | mm | 900 ÷ 1200 | 600 ÷ 1200 |  |  |

## Fences

| overall height | mm | 2145 |
| --- | --- | --- |
| height from floor | mm | 165 |
| execution of door |  | one wing door right, one wing door left, two wing doors, sliding door right, sliding door left |
| width of doors | mm | 800 one wing |
| widths of fence parts | mm | 1000, 800, 650, 500, 300, |
| sieve mesh size | mm | 40×40 |
| thickness of fencing | mm | 3.1 |

## Service footbridge

| type | 1700 | 2300 | 3000 |
| --- | --- | --- | --- |
| max. load | kg | – | 175 | 175 |
| width | mm | – | 600 | 600 |
| length | mm | – | 3300 | 3760 |
| height of banisters | mm | – | 1000 | 1000 |
| access |  | ladder |

# Communication signals

## Without conveyor control

### INPUT SIGNALS from conveyor to wrapper

- Start of wrapping

- Possible to wrap (external stop)

- Assortment 1

- Assortment 2

- Assortment 3

- Fencing doors closed

- Emergency stop- disconnect, if neighbourhood  is in emergency stopping

2 switching contacts 24V DC 5A – on terminal block of switchboard

Note: 	Signals are realized by one switching contact 24V DC 200mA placed in switchbox cabinet of conveyor.

Signals Assortment 1, Assortment 2, and Assortment 3 are optional, using combinations of these signals is possible to choose one of 8 preset wrapping programs (if this function is not used program nr. 0 will be started).

If Possible to wrap signal is inactive, all movements of machine are blocked, running program is interrupted, interrupted program is terminated by following descending edge of Possible to wrap signal.

### OUTPUT SIGNALS from wrapper to conveyor

- Conveyor free  	- signalize state where nothing obstructs free passage of pallet under machine.

- End of wrapping

- Failure 	- disconnect when any failure on wrapper occurs (for ex. out of film, opened covers)

- Emergency stop	- disconnect when wrapper is in emergency stopping.

2 switching contacts 24V DC 5A – on terminal block of switchboard

Note: 	Signals are realized by one switching contact 24V DC 200mA placed in switchbox cabinet of wrapper.

When machine is switched off all signals has logical value 0.

### FUNCTIONS OF MACHINE

- If Conveyor free then system control of conveyors can send pallet into machine.

- Conveyor control system stop pallet in the middle of wrapping area.

- Conveyor control system order Start of wrapping (impulse 1s is enough).

- Wrapping machine accomplish programmed wrapping cycle.

- Wrapping machine report End of wrapping (impulse 1s is enough).

- If Conveyor free is on conveyor control system can out feed the pallet.

| Conveyor -> wrapper |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Start of wrapping |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Wrapping is possible (external stop) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Wrapper -> Conveyor |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Conveyor free |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| End of wrapping |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Action |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Conveyor below wrapper |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Wrapping |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

## With control of conveyors (per order)

Wrapper controls its conveyor.

Conveyors before and behind of wrapper controls neighbouring line (thereinafter neighbouring).

### SIGNALS from neighbourhood to wrapper

- Palette on entrance (permanent signal) – on the conveyor before wrapper is palette ready for sending on wrapper conveyor

- Free on exit (permanent signal) - conveyor behind wrapper is free

- Palette received on exit (pulse1s) – palette reach sensor on conveyor behind wrapper

- Assortment 1

- Assortment 2

- Assortment 3

- Emergency stop - disconnect, if neighbourhood  is in emergency stopping

2 switching contacts 24V DC 5A – on terminal block of switchbox cabinet

Note: 	Signals are realized by one switching contact 24V DC 200mA placed in switchbox cabinet of conveyor.

Signals Assortment 1, Assortment 2, and Assortment 3 are optional, by their combinations is possible remotely choose one of 8 preset wrapping programs (if they are not used, program No. 0 will be started). The wrapping machine scans the status of signals of the goods range during the travel of the pallets from the conveyor of the superior line to the first conveyor of the wrapping machine (the signal must be constant during the whole period of the pallet travel)

### SIGNALS from wrapper to neighbourhood

- Free on entrance (permanent signal) – wrapper conveyor is free

- Palette received on entrance (impulse 1s) - palette reach sensor on wrapper conveyor

- Palette on exit (permanent signal) – on wrapper conveyor is palette ready for sending on conveyor behind wrapper

- (Emergency stop) - disconnect, if neighbourhood  is in emergency stopping

2 switching contacts 24V DC 5A – on terminal block of switchbox cabinet

Note: 	Signals are realized by one switching contact 24V DC 200mA placed in switchbox cabinet of wrapper.

Signals have logical value 0 in manual mode and when the machine is switched off

### FUNCTIONS OF LINE

- Feeding in of palette is possible if Palette is on entrance and is Free on entrance (it does not matter, which command occurs earlier).

- Neighbourhood starts conveyor before wrapper, wrapper start   conveyor of wrapper – palette is feeding in on wrapper conveyor.

- If during feeding in one of the signal Palette on entrance or Free on entrance falls down, moving of pallets is stopped. After restoring of the signal is possible to continue.

- Pallet is stopped on pallet sensor on wrapper conveyor, wrapping machine answers Pallet received on entrance (signal 1s), feeding in is finished by this way.

- Feed out of the pallet is possible if the Palette is on exit and if is Free on exit (does not matter, which command occurs earlier).

- Wrapper starts wrapper conveyor, neighbourhood starts conveyor behind wrapper – pallet is feeding out on conveyor behind wrapper.

- If during feeding out of the pallet falls down one of the signal Palette on exit or Free on exit, moving of pallets is stopped. After restoring of the signal is possible to continue.

- Pallet stops on sensor of the pallet on conveyor behind wrapper, neighbourhood answers Palette received on exit (signal 1s), feeding out is finished by this way.

Note: 	If wrapper controls more conveyors:

- for feeding in:  wrapper conveyor = first conveyor controlled by wrapper

- for feeding out: wrapper conveyor = last conveyor controlled by wrapper

- Pallets are moved in sequence from previous conveyor to the next conveyor (if it is free).

If pallets are taken off from conveyor controlled by wrapper:

- description of the function for exit and signals are not valid

- feeding out conveyor is considered as busy 20s yet (it is possible to adjust) after pallet is taken off- replace sensor of the fork lift.

| Conveyor -> wrapper |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Palette on entrance |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Free on exit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pallette received on exit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Wrapper -> conveyor |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Free on entrance |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pallet received on entrance |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pallette on exit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Action |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Conveyor before wrapper |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Conveyor below wrapper |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Conveyor behind wrapper |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

### INITIALISATION OF THE LINE

Initialisation runs after each start of wrapper and each switchover in to automatic mode – wrapper trays to find loss pallets (in between conveyors or between sensors).

Initialisation is unable to solve all failure states, due to this   operator attendance is necessary.

- Operator check state of wrapper, switchover wrapper in to manual mode, sets wrapper in to initial position (if it is necessary) and switchover back in to automatic mode.

- Conveyors, which does not have screened sensor, are set in to motion for 10s.

- Pallet stops on the nearest sensor, if the pallet was between sensors.

- If pallet was on boundary line of conveyors, next conveyor is started and trays to pull over the pallet.

- Operator has to check position of the pallets after finishing of initialisation, eventually adjust their position in manual mode.

- If there is a busy conveyor in wrapping space, operator must decide if to wrap pallet or to send away.

- Wrapper gives communication signals in to neighbourhood after finishing of initialisation.

## Operation of the Machine during Switch-Over from Automatic Mode to the Manual Mode and Back in Dependence on Configuration of the Line

A. Conveying tracks only inside the safety area of the wrapping machine (1 switch R/A)

1. Switch of the manual and automatic mode for the wrapping machine

Switch-over from the automatic mode to the manual mode

- the wrapping machine stops

- tracks stop (the system remembers positions of the pallets according to shading of the sensors)

- Manual functions of wrapping machine as well as of tracks are available

Switch-over from the manual mode to the automatic mode

- Inquiry  - Tracks Continue / Initialize:

- - Continue – tracks continue in the operation before switch-over to the manual mode *).

- - Initialize – system forgets the positions of the individual pallets and searches for their positions again.

- Inquiry – Wrap the pallet Yes/No.

- - Yes – the wrapping machine wraps the pallet.

- - No – wraps machine considers the pallet as wrapped and removes it.

B. Conveying tracks inside and outside the safety area of the wrapping machine (2 switches R/A) (per order)

1. Switch of the manual and automatic mode for the wrapping machine

Switch-over from the automatic mode to the manual mode

- the wrapping machine stops

- tracks inside the safety area of the wrapping machine stop (the system remembers positions of the pallets according to shading of the sensors)

- only manual functions of the wrapping machine are available

Switch-over from the manual mode to the automatic mode

- Inquiry – Tracks in the wrapping machine area Continue. (only when the switch for tracks mode is in position Automatic mode)

- - Continue – tracks continue in operation before switch-over to the manual mode *).

- Inquiry – Wrap the pallet Yes/No.

2. Switch of the manual and automatic mode for the tracks

Switch-over from the automatic mode to the manual mode

- All tracks stop (the system remembers positions of the pallets according to shading of the sensors)

- It serves only for holding of the operation of track program – for access to manual functions it is necessary to switch the machine to the manual mode.

Switch-over from the manual mode to the automatic mode

- Inquiry – Tracks Continue/Initialize

*) In case that shading of sensors does not correspond to the remembered status, the control system will request initialization or correction in the manual mode.